Elementary Encraption 2
Implementing a Columnar Transposition in C
Dr. Peter A. H. Peterson <pahp@d.umn.edu>
University of Minnesota Duluth

Overview
In this exercise, you will implement a Columnar Transposition Cipher (CT) in C. This will give you hands-on experience implementing transposition ciphers and coping with aspects of block ciphers, such as padding.

A video introduction to this lab is at: https://www.youtube.com/watch?v=QeDI-zsUuO8

A Columnar Transposition (CT) works by writing symbols into a grid of a particular size (which we call a transposition box), moving to a lower row when an upper row is full. Once the box itself is full, it is read out in columns top to bottom, left to right (hence the name). For example, given the input “abcdefghijklmnop” and a 4x4 grid, a CT cipher would perform the following process:

Input	Transformation Box	Output
abcdefghijklmnop →	a b c d / e f g h / i j k l / m n o p	→ aeimbfjncgkodhlp

CT ciphers are distinct from the Caesar and Vigenère ciphers in at least two important ways. First, CT ciphers perform transposition, unlike Caesar and Vigenère which only perform substitution. Secondly, CT ciphers are block ciphers in that the block cannot be written out until the P-box (permutation box) is full or sufficiently padded. The latter means that, while Caesar and Vigenère ciphertext can be written letter by letter (a stream cipher), CT ciphertext will be written out in discrete blocks (a block cipher). This will require padding the input so that its size is a multiple of the blocksize. (See Requirements, below.)

Requirements
Code and Compilation

Your submission will be electronically graded for correctness and uniqueness. Therefore, your code must successfully compile on the MWAH 187 machines running Ubuntu and must follow the following requirements.

1. It must be submitted as a C source file (.c plain text), not as a PDF, .doc, .docx, etc.
2. Your code must not use any of the Banned Functions listed in the Vigenère Encraption lab manual or it will be scored a zero (0).
3. You need to create a single C source file capable of generating object files for both an encoder and decoder. Your code will be compiled using the commands

   gcc columnar.c -o encoder -D MODE=ENCODE and
   gcc columnar.c -o decoder -D MODE=DECODE

   See the Appendix of the Vigenère lab manual for instructions to do this.
4. Your code should not use any libraries other than stdio, stdlib, string, errno and limits (in particular, it should not require any additional flags to the compiler or modifications to the test script to compile).
5. Your code should not create any temporary files during encryption or decryption.
6. You must NOT use other online examples of the Columnar Transposition as a coding template; if you do not understand how the TC works, talk to your instructor or TA.
7. Instead of keys, the dimension of the transposition box will be specified on the command line.
8. The transposition box dimension will be between 1 and 10.
9. Input will not be limited to text only (i.e., test using binary data like applications or images).
10. Input will not be limited to any particular length (i.e., test using large files).
11. Your main() function should return 0 in the case of a successful exit.

Encoder and Decoder
Your encoder and decoder must take the following parameters as input:
1. The number of rows and columns in the transposition box, e.g., 4. (The box will be a square.)
2. A path to an input file, e.g., /tmp/input
3. A path to an output file, e.g., /tmp/output
4. Upon running ./encoder 4 /tmp/input /tmp/output, output should contain the contents of input as encoded using a 4x4 transposition box. Upon running
   ./decoder 4 /tmp/encoded /tmp/decoded, /tmp/decoded should contain the contents of encoded as decoded using a 4x4 transposition box.

Padding
Block Ciphers encrypt and decrypt a fixed number of bytes at once. If there is not enough input to fill whole blocks, a block cipher must pad the input before encrypting it. However, this padding must be done in a way that can be undone upon decryption. In other words, the original length of the file must be able to be recovered.

If x is the number of columns and y is the number of rows in your transposition box, your CT cipher should read in xy bytes of input at once and then encrypt it. If there are not xy bytes of input available, you should pad the remaining space in the buffer by inserting one byte 'X' (serving as a flag) followed by as many 'Y' bytes required to fill the block. If the plaintext fills the last block completely, your cipher should create a complete “padding block” consisting of 'X' followed by enough 'Y' bytes to fill the block. To be completely explicit, by 'X' we mean the character 'X' and by 'Y' we mean the character ‘Y’. In other words, to write your padding you will use code like array[i] = 'X' or array[i] = 'Y'.

Note: this means that you’ll always have to add padding. Either you’ll add it to the last block of input, or you’ll add a full padding block after the input ends.

With this scheme, there will always be padding to remove from the last block. This means that you need a way to know when the last block is being encrypted (so that you can add padding) and decrypted (so that you can remove padding). After the last block is decrypted, remove any trailing 'Y' bytes (if they exist) and then the last 'X' byte (which must always exist in the last block). (This particular approach to padding was suggested by Schneier and Ferguson.)

Padding Examples:

In these examples, assume a four-byte (2x2) block.

- Final block: “ABCD”. There is no room for padding, so add a full padding block “XYYY” to the plaintext before encryption. On decryption, the second to the last block will decrypt “ABCD”. The final block will decrypt “XYYY” and should be dropped completely (i.e., not written to disk).
- Final block: “00”. Pad the last plaintext block before encryption so that it reads “00XY”. After decryption, “00XY” will be the last block. Remove any trailing Ys and the final X so that it reads: “00”
- Final block: “X”. Pad the last plaintext block before encryption so that it reads “XXYY”. After decryption, remove the trailing Ys and the final X so that it reads “X”.

Note: knowing when you’re decrypting the last block requires you to know the size of the input. By keeping track of how many bytes you have left, you can determine when you are decrypting the last block. See “Finding the Length of the Input File”, below.
Sample Vectors

Sample vectors (i.e., transposition box sizes and input along with correctly encrypted and decrypted data) will be provided at

http://lars.d.umn.edu/labs/columnar-vectors.tar.gz

for correctness testing. Put your columnar.c code into the columnar-vectors directory and run ./test.sh. If you would like the script to quit on the first error, use the -q switch. If you would like to perform “padding only” testing (see hints, below), add the -p switch. See the included README.txt for more information.

Grading will use the sample vectors provided and may use new untested vectors. Therefore, you should test your code against the sample vectors and various other types of input and keys that you choose.

Submission
Submit your source code for columnar.c via Moodle by the due date specified.
Hints & Tips
Use Helper Functions!

While it is not required, your code will be much more manageable and easier to debug if you create and use/reuse helper functions rather than writing one huge function with lots of repeated code. While it might be longer, it will be easier to write and understand.

For example, my solution uses the following functions:
Padding and Unpadding Blocks

int pad_buffer(char *buffer, unsigned int bufsize,
unsigned int rbuf_index)
int unpad_buffer(char *buffer, unsigned int bufsize)

Write a function pad_buffer() that takes as input a buffer of size bufsize bytes where rbuf_index indicates the first empty byte in the buffer. It writes an 'X' into buffer[rbuf_index] and fills the remaining bytes with 'Y' characters. Then write a function unpad_buffer() that removes padding from a buffer. An easy way to do this is to start at the end of the buffer and work backwards, removing all contiguous ‘Y’ bytes and one ‘X’ byte. Both functions modify (in place) the memory pointed to by the pointer buffer and return the number of padding bytes added or removed.
Transposing Blocks

void transpose_buffer(char *out, char *in, unsigned int dim)
transpose_buffer takes a dim by dim sized buffer in and performs the Columnar Transposition into the same-sized buffer out. It modifies out in place and returns nothing. Since the Columnar Transposition is symmetric, you do not need a special untranspose_buffer() function. There are multiple ways to implement transposition; see “Two Transposition Methods,” below.
Writing Blocks of Output
int dump_buffer(char *buffer, unsigned int bufsize,
unsigned int bytes, char *output_path)

dump_buffer takes in buffer and appends bytes bytes from buffer to the file named in output_path. It then erases buffer using memset(buffer, 0, bufsize). It returns the number of bytes written.

Other Helper Functions

I also have helper functions to print out a block of data in ASCII and hexadecimal for debugging purposes. You can use the %x format in a printf() to print a char in hex.

Two Transposition Methods
Two-dimensional Arrays

There are two obvious ways to handle transposition. Each has drawbacks.

The first method is to use two dimensional arrays. You can create two-dimensional arrays to create and manipulate your transposition box. Do this in C as follows:

char box[numcols][numrows]

Then, you can write into the grid by indexing into the 2D array as follows:

box[x][y] = symbol

You can read from the grid as follows:

cipher = box[0][0]

... which would be the “top left” character in the transposition box.

When filling the box, write rows in order, When performing the transposition, you will read the columns instead. You can “loop” your array indexes using the box dimensions and modular arithmetic.

The drawback to 2D arrays is that it is not straightforward to pass them to functions, which means that it is less easy to use helper functions in your code. However, if you always read in from a character array and output to a character array (only using the 2D array within the transposition function) you can work around this limitation.
One-dimensional Array + Transposition Algorithm

The second obvious approach is to determine the general permutation algorithm for the columnar cipher for a box dimension of n. Then, you can swap characters from one 1D array directly to their new positions in another 1D array. In the C language, it is very easy to pass arrays by passing a pointer, so it is easy to make helper functions to make your code simpler. However, to do this you must first determine the transposition algorithm!
Finding the Length of the Input File

While you can write perfectly correct code that does not ever explicitly check the length of the file, you might find it helpful to know when you're about to reach the end of your input. C provides functions for finding the length of a file in bytes. Here's an easy way to do it. First, make sure you include the following headers at the beginning of your program:

#include <sys/types.h>
#include <sys/stat.h>
#include <unistd.h>

We're going to use the stat() function, which fills a struct stat. A structure is a fixed-size data structure with named members, which can have different types (e.g., char, int, etc.). A stat structure, then, is a data structure designed to hold numerous pieces of information relating to the file. (See man fstat for more information.) All we care about is the size in bytes, which is the st_size structure member. First, you need to declare a structure of type stat, named (here) filestats:

struct stat filestats;

Then, when you call stat(), we will pass a pointer to filestats. The pointer is the memory address of the variable, which we can access using the '&' operator:

int err;
if ((err = stat(input, &filestats)) < 0) {
printf("error statting file! Error: %d\n", err);
}

If the stat() call succeeds, the structure will be filled with the various pieces of information. We can access them by name, such as by printing out filestats.st_size, which we can treat as an integer of type long unsigned:

printf("Size of input is: %lu bytes\n", filestats.st_size);

This should help you determine when to add or remove block padding.

Converting String Parameters to Integers

The transposition box dimension will be the first parameter on the command line, stored in the character array argv[1]. However, this means that the first parameter will be a string “n” (the string the user entered on the command line) instead of an integer n. To convert the string (or ASCII) representation of the number into an integer, use the function atoi(), like so:

int dimension;
dimension = atoi(argv[1]);

Add and Test Using a “Padding Only” Mode

There are two challenges to this assignment: getting the transposition code right and getting the padding code right. Transposition cannot work properly without padding first working properly. Recognizing this, I added a “padding only” test mode to the test script, which you can invoke using the -p option. When using the “padding only” mode, the test script simply ensures that your code adds and removes the padding properly. Accordingly, the test vectors include “correct” versions of padding.

You could test in “padding only” mode when you have working padding code (but before you have transposition code). Or, you can add a fourth argument to your code that dynamically enables and disables “padding only” mode. For example, when executing ./encoder 4 /tmp/input /tmp/output 1 or ./decoder 4 /tmp/ciphertext /tmp/plaintext 1 (note the 1 at the end of each command) my solution performs padding but not transposition. This is compatible with the test script as long as your program does not require the additional parameter to function properly.

Again, adding a “padding mode” is optional, but -- believe me -- the trivial amount of extra code could save you hours of debugging.

Padding Hints

You must always add and remove padding to every input! If an input ends on a block boundary, you still need to add a full block of padding. However, DON'T try to add padding to the original input file or a copy. This is slow and inefficient. Instead, keep track of where you are in the file (either by counting bytes or waiting until you reach EOF), and simply add padding to the final block of input (or after the final input if necessary).

When decrypting, you should decrypt each block one at a time and only unpad the very last block (which must have padding).

Again, you can easily keep track of this by getting the file length and keeping track of where you are in the file using a variable.

Code Running Slow?

Is your code running slowly? Large inputs, especially with a 1x1 box, can have poor performance, especially if debugging code is enabled. Consider disabling debugging code when running tests and when submitting your final code.